## Slide 1: Introduction to Future Technology Transformations FTT – Part (2)
Pim Vercoulen ピムバクレン
p.vercoulen@student.ru.nl
June 3rd, 2018 ASSIA office Nagoya University 名古屋大学

## Slide 2: Outline for today
Recap of last FTT:Seminar
FTT:Steel
  Preliminary results on China, Japan, Korea, and Taiwan
  The data that is still sought for
FTT:Power
  Working with the varying policies
    Subsidy + demand policies
    Exogenous capacity additions (e.g. government enforced) + Regulations
    Carbon tax + Feed-in-Tariff

## Slide 3: Recap of last week
Methodology of FTT framework
  Levelised cost
  Preference Matrix
  Change in market share
Preliminary Results of FTT:Steel
  Many data gaps still exists
Working with FTT:Power
  We’ve used subsidies / taxes on capital investment costs
  Regulations on coal power

## Slide 4: FTT:Steel – China – Current status

## Slide 5: FTT:Steel – China – Challenges
Low scrap availability
Low quality of domestic iron ore and coal
Overcapacity -> Utilisation rates of 50% were reported! (OECD 2015)
Chart: China
| 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Scrap:Production | 0.026936 | 0.029845 | 0.031278 | 0.032714 | 0.031817 | 0.030786 | 0.031772 | 0.03368 | 0.033026 | 0.035175 | 0.041752 | 0.048417 | 0.056281 | 0.066829 | 0.080387 | 0.10169 | 0.11797 | 0.13982 | 0.14027 | 0.15358 | 0.16834 | 0.18308 | 0.18933 | 0.2117 | 0.21113 | 0.21076 | 0.22 | 0.22995 | 0.24058 | 0.25186 | 0.26375 | 0.27619 | 0.28911 | 0.30242 | 0.31602 | 0.3298
Steel production | 822690 | 858749.7533 | 896115.6201 | 934632.8296 | 974118.7872 | 1014363.3357 | 1055129.8394 | 1096157.1654 | 1137162.6046 | 1177845.7351 | 1217893.1858 | 1256984.208 | 1294796.9164 | 1331015.012 | 1365334.763 | 1397471.9901 | 1427168.7857 | 1454199.6991 | 1478377.1312 | 1499555.7183 | 1517635.5251 | 1532563.9275 | 1544336.1254 | 1552994.2935 | 1558625.4429 | 1561358.1198 | 1561358.1198 | 1558823.4273 | 1553978.6108 | 1547068.9129 | 1538354.2611 | 1528103.4128 | 1516588.4128 | 1504079.5122 | 1490840.6548 | 1477125.6019
Scrap availability | 22160 | 25629.6 | 28028.4 | 30575.2 | 30994 | 31228.4 | 33523.2 | 36918.4 | 37556 | 41430.8 | 50849.6 | 60859.2 | 72872.8 | 88950.4 | 109755.6 | 142114 | 168366.8 | 203324.8 | 207365.2 | 230306 | 255476.4 | 280584.4 | 292392.4 | 328774.4 | 329076 | 329076 | 343499.9013 | 358446.248 | 373853.1318 | 389647.5149 | 405745.3343 | 422051.9358 | 438462.8662 | 454865.0418 | 471138.294 | 487157.2743

## Slide 6: FTT:Steel – China – Policies
Nationally Determined Contribution to the Paris Accord:
  Reduce emission intensity (GtCO2/GDP)
    This doesn’t mean a reduction in absolute emissions
  Reach peak emission before 2030 and reduce afterwards
  Increase energy efficiency (GJ/tcs)
Reduce overcapacity
  Closing down small (i.e. inefficient) plants to increase the utilisation rate
  Merge small to medium steel companies to large ones

## Slide 7: FTT:Steel – Japan – Current status

## Slide 8: FTT:Steel – Japan – Challenges
Lack of domestic raw materials
Export to the US might become a problem because of steel tariffs
More room for the secondary production routes to grow, probably not enough to become self-reliant though
Chart: Japan
| 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Scrap:Production | 0.39882 | 0.38474 | 0.33437 | 0.32982 | 0.31642 | 0.31843 | 0.3016 | 0.31135 | 0.2722 | 0.26821 | 0.29711 | 0.28195 | 0.29056 | 0.29377 | 0.29594 | 0.29222 | 0.2994 | 0.30759 | 0.30237 | 0.22221 | 0.2778 | 0.27274 | 0.27218 | 0.28144 | 0.28265 | 0.28395 | 0.29405 | 0.30459 | 0.31546 | 0.32655 | 0.33774 | 0.3489 | 0.35988 | 0.37056 | 0.38077 | 0.39039
Steel production | 110666 | 113998.1033 | 117392.1973 | 120822.1344 | 124259.5855 | 127674.4535 | 131035.3931 | 134310.4286 | 137467.6521 | 140475.981 | 143305.9443 | 145930.4664 | 148325.6127 | 150471.2602 | 152351.6633 | 153955.8832 | 155278.0624 | 156317.5306 | 157078.7386 | 157571.0275 | 157808.2471 | 157808.2471 | 157592.2682 | 157184.2653 | 156610.1938 | 155897.2914 | 155073.3824 | 154166.2275 | 153202.9384 | 152209.4686 | 151210.1874 | 150227.5392 | 149281.7849 | 148390.8209 | 147570.0655 | 146832.4065
Scrap availability | 44135.6 | 43859.6 | 39252.8 | 39849.2 | 39317.6 | 40656 | 39520.4 | 41817.6 | 37419.2 | 37676.8 | 42577.6 | 41144.8 | 43098 | 44204.4 | 45087.2 | 44988.4 | 46490.4 | 48081.2 | 47495.6 | 35013.6 | 43839.6 | 43040.4 | 42892.8 | 44238 | 44266.4 | 44266.4 | 45599.2413 | 46956.8789 | 48328.8538 | 49703.8342 | 51069.7814 | 52414.1573 | 53724.1714 | 54987.0609 | 56190.3924 | 57322.3777

## Slide 9: FTT:Steel – Japan – Policies
NDC target of 26% GHG emission reduction by 2030 compared to 2013
  Steel sector specifically addressed:
    Efficiency improvement of electricity-consuming facilities
    More chemical recycling of waste plastic at steel plants
    Introduction of next-generation coke making
    Improvement of power generation efficiency process (SCOPE21)
    Enhanced energy efficiency and conservation facilities
    Introduction of innovative ironmaking process (Ferro Coke)
    Introduction of environmentally harmonized steelmaking process (COURSE50)
COURSE50
  Voluntary action taken by the steel industry to focus on new, low-carbon technologies
  GHG emission reduction target of 30% by 2050

## Slide 10: FTT:Steel – Korea – Current status

## Slide 11: FTT:Steel – Korea – Challenges
Exempted from US steel tariffs

## Slide 12: FTT:Steel – Korea – Policies
GHG emission reduction targets:
  30% below BAU by 2020
  37% below BAU by 2030.
Emission Trading Scheme
  Includes the iron and steel industry

## Slide 13: FTT:Steel – Taiwan – Current status

## Slide 14: FTT:Steel – Taiwan – Challenges
Relies on import of resources
Taiwan is at risk of being affected by US steel tariffs

## Slide 15: FTT:Steel – Taiwan – Policies
No NDC, but a unilateral voluntary contribution
  “Greenhouse Gas Reduction and Management Act”
    Reduce GHG emissions by 50% compared to BAU in 2050

## Slide 16: Data needs
Historical utilisation of technologies is not well reported. Examples:
  In Korea FINEX is used (designated as a SRI+ - BOF route), but no timeline of steel production by this technology can be found.
  The same for COREX (designated as SRI-BOF) in Korea and China.
  And Hismelt (designated as SRI-BOF) in China
Accurate data on anything that could affect the levelised cost of steelmaking:
  Regional specific investment costs
  Operation and maintenance
  But most importantly, material consumption

## Slide 17: FTT:Power – Policy setting examples
Now back to policy setting with FTT:Power

## Slide 18: FTT:Power – Recap of last week – Baseline Results

## Slide 19: FTT:Power – Recap of last week – S1 Results

## Slide 20: FTT:Power – S2– Subsidy + Demand
Scope : Japan (No. 35) and China (No. 41)
Goal : Incentivize renewables (…and cheat a little bit)
Policies
  Subsidies on investment costs:
    75% for all solar and wind technologies (enter: -0,75)
  Electricity storage to capacity ratio (MEES and MEKS):
    Japan: 1% in 2018. Let it increase by 2% annually until 50% is reached
    China: 30% in 2018. Let it increase by 0,25% annually
Evaluate Emissions, Electricity Price, Market shares of Coal and Renewables (solar and wind), and Total Installed Capacity
  Realize that changes occur due to technological diffusion which are driven by the LCOE

## Slide 21: FTT:Power – S2– Subsidy + Demand – Results

## Slide 22: FTT:Power – S3– Capacity additions + Regulations
Scope : Japan (No. 35) and China (No. 41)
Goal : Substitute Coal for its CCS variant
Policies
  Regulations:
    Coal:
      Japan: 85 GW in 2018 and a 2,5 GW annual decrease
      China: 750 GW in 2018 and a 20 GW annual decrease
  MWKA:
    Coal (CCS):
      Japan: 5 GW in 2018 and a 3,75 GW annual increase
      China: 40 GW in 2018 and a 30 GW annual increase
Evaluate Emissions, Electricity Price, Market shares of Coal and Renewables (solar and wind), and Total Installed Capacity
  Realize that changes occur due to technological diffusion which are driven by the LCOE

## Slide 23: FTT:Power – S3– Capacity additions + Regulations – Results

## Slide 24: FTT:Power – S4– Carbon Tax + Feed-in-Tariff
Scope : Japan (No. 35) and China (No. 41)
Goal : Incentivize renewables
Policies
  Carbon tax:
    For both China and Japan: 55 €/tC in 2018 and increase by 6.5% annually.
  Feed-in-Tariff
    Solar: From 2018 onwards enter 75 for all solar technologies
    Wind: From 2018 onwards enter 75 for all wind technologies
Evaluate Emissions, Electricity Price, Market shares of Coal and Renewables (solar and wind), and Total Installed Capacity
  Realize that changes occur due to technological diffusion which are driven by the LCOE

## Slide 25: FTT:Power – S4– Carbon Tax + Feed-in-Tariff – Results

## Slide 26: FTT:Power – Overview of results
 |  | Japan |  |  |  |  |  | China |  |  |  |  | 
 |  | S0 |  | S1 | S2 | S3 | S4 | S0 |  | S1 | S2 | S3 | S4
 |  | 2018 | 2050 | 2050 | 2050 | 2050 | 2050 | 2018 | 2050 | 2050 | 2050 | 2050 | 2050
Emissions | Gt/yr | 0,686 | 0,876 | 0,627 | 0,391 | 0,510 | 0,616 | 4,792 | 10,42 | 4,704 | 7,383 | 4,107 | 7,903
Electricity price | $13 / MWh | 113,7 | 110,3 | 126 | 108,7 | 103,7 | 144,1 | 77,74 | 90,5 | 438,2 | 366,3 | 115 | 241,5
Share of renewables | % | 2,8% | 6,2 | 29,2 | 59,9 | 1,6 | 28,2 | 4,8% | 6,5 | 44,8 | 33,3 | 18,3 | 24
Share of Coal | % | 32,5% | 32,7 | 6,7 | 5,5 | 5,3 | 8,6 | 65,4% | 64,8 | 11,7 | 32,8 | 14,9 | 40,2
Total installed capacity | GW | 270,5 | 350,7 | 380,7 | 757,1 | 347,5 | 381,2 | 1407 | 3026 | 4239 | 4080 | 3232 | 3501

## Slide 27: FTT:Power – Overview of results
S0: Baseline
S1: Regulations on Coal in combination with taxes on technologies that might replace it
S2: Subsidies on renewables and an increase in storage capacity
S3: Regulations on Coal mitigated by exogenous capacity additions on Coal + CSS
S4: Carbon tax in combination with Feed-in-Tariffs on renewables
Japan
  Best scenario might be S2 for Japan, while it doesn’t work that well for China
China
  Best scenario might be S3 for China, which also works for Japan to some degree